## Slide 1
Connect to GND Pin
Connect 2 wires to door controller
Use the same connection as your existing garage door switch
Garage Door Relay Switch Connections
Shielded solid copper wire from terminal strip to door controller
VCC
GND
IN1
IN2
Garage Door Switch to GPIO 5
Connect to 5v Pin

## Slide 2
Connect to 3.3v Pin
Garage Door Sensor Connections
Female jumper cables connect to GPIO Pins
Solid copper wire connects to female jumper
Distance between magnets needs to be at least 2mm
Magnet connected to trolley
Connect to GPIO 24